## Slide 1: Loom: Flexible and Efficient NIC Packet Scheduling
——Presented by Xinchen Wan

## Slide 2: Outline
Background
Contributions
Evaluation
Conclusion
Weakness

## Slide 3: Background
Aim: In multi-tenants environment, it’s desirable to achieve high-throughput, low latency and tenants’ fairness
1. What is current NIC problem?
  Single Queue NIC packet scheduling
  MultiQueue NIC packet scheduling

## Slide 4: Single Queue NIC Packet Scheduling Limitations
Single queue throughput is limited
  Especially with very small packets
  Lack scalability
Software scheduling consumes CPU
Core-to-core communication increases latency
CPU
NIC
Wire
App 1 App 2
NIC
SQ struggles to drive line-rate

## Slide 5: MultiQueue NIC Packet Scheduling Limitations
Multi-Queue NICs enable parallelism
Multi-Queue NICs have packet scheduler that choose which queue to send packets
MQ struggles to enforce policies

## Slide 6: MultiQueue NIC Struggles to enforce policies
Rate-limit Policy
Network traffic is not uniformly spread across application threads.
Notes: 对一个16线程的memcached程序进行限速，理想状况是整体流速限制在2Gbps

## Slide 7: MultiQueue NIC Struggles to enforce policies
Per-queue fair scheduling policy
MQ
QPF
Active flows are not uniformly spread across the cores.
Each job doesn’t have same number of active flows.
Notes: 运行两个spark程序，希望达到共享网络带宽.

## Slide 8: Background
1. What is current NIC problem?
2. Why offload all packet scheduling on NIC?

## Slide 9: Why offload all packet scheduling on NIC?
MQ-Pri: Strict priority in hardware, fairness in software.
MQ-ETS: Fairness in hardware, strict priority in software.
Two tenants:
One runs Spark.
The other runs Spark and memcached.
Require:
1. Fairness for two tenants.
2. Memcached has higher priority

## Slide 10: Loom is a new NIC design that moves all per-flow scheduling decisions out of the OS and into the NIC
Loom uses a queue per flow and offloads all packet scheduling to the NIC

## Slide 11: Contributions
1. Specification: A new network policy abstraction: restricted directed acyclic graphs(DAGs)
2. Enforcement: A new programmable packet scheduling hierarchy designed for NICs
3. Updating: A new expressive and efficient OS/NIC interface

## Slide 12: Contributions
1. Specification: A new network policy abstraction: restricted directed acyclic graphs(DAGs)
2. Enforcement: A new programmable packet scheduling hierarchy designed for NICs
3. Updating: A new expressive and efficient OS/NIC interface

## Slide 13: Loom policy DAG
Scheduling nodes: Work-conserving policies for sharing the local link bandwidth
Shaping nodes: Rate-limiting policies for sharing the network core (WAN and DCN)
Programmability: Every node is programmable with a custom enqueue and dequeue function
Two types of nodes:
Fair_1
Wire
Pri_1
VM2
VM1 VM1
FIFO_1
RL_WAN
RL_None
Shaping Node
Scheduling Node

## Slide 14: Loom: Policy Abstraction
DAG restriction: Scheduling nodes form a tree when the shaping nodes are removed
(b) and (d) are prevented because they allow parents to reorder packets that were already ordered by a child node.

## Slide 15: Contributions
1. Specification: A new network policy abstraction: restricted directed acyclic graphs(DAGs)
2. Enforcement: A new programmable packet scheduling hierarchy designed for NICs
3. Updating: A new expressive and efficient OS/NIC interface

## Slide 16: Loom enforcement challenge
No existing hardware scheduler can efficiently enforce Loom Policy DAGs
Domino PIFO Block
1 x 1 x
Scheduling Shaping
Scheduling
New PIFO Block?
1 x
Shaping
N x
To implement Loom, there should be a lot of shaping queues in the hardware, which may exists the queue
number size in NIC.

## Slide 17: Insight: All shaping can be done with a single queue because all shaping can use wall clock time as a rank

## Slide 18
Solution: Set a global shaping queue in PIFO
Procedures:
All traffic is first only placed in scheduling queues
If a packet is dequeued before its shaping time, it is placed in a global shaping queue
After shaping, the packet is placed back in scheduling queues
Notes: Extra enqueue and dequeue operations
T2, no packet is transferred
What if there exists another packet at head at TD2?
What if the number of rate-limit packets exceeds the shaping queue size?

## Slide 19: Contributions
1. Specification: A new network policy abstraction: restricted directed acyclic graphs(DAGs)
2. Enforcement: A new programmable packet scheduling hierarchy designed for NICs
3. Updating: A new expressive and efficient OS/NIC interface

## Slide 20: PCIe Limitations
NIC doorbell and update limitations:1
NIC
App
Core
DB1
DB2
DB3
DB4
…
DB_F
PCIe
1
PCIe
Engine
2
1
Latency Limitations:
120-900ns
2
Throughput Limitations:
~3Mops (Intel XL710 40Gbps)
PSPAT: software packet scheduling at hardware speed
Luigi Rizzo1, Paolo Valente2, Giuseppe Lettieri1, Vincenzo Maffione2 1Univ. di Pisa, 2Univ.di Modena e Reggio Emilia
rizzo.unipi@gmail.com. Work supported by H2020 project SSICLOPS.
1

## Slide 21: Batched Doorbells
Using on-NIC Doorbell FIFOs allows for updates to different queues(flows) to be batched
NIC
Per-core Doorbell
FIFO
App
Core
PCIe

## Slide 22: Inline Metadata
Scheduling metadata (traffic class and scheduling updates) is inlined to reduce PCIe writes
Desciptor inlining allows for scheduling before reading packet data
NIC
DMA Engine
PIFOs
Mem
Q5
Q_F
…
Q1
Q2 Q3
Wire

## Slide 23: Evaluation
Software prototype of Loom in Linux on the Berkeley Extensible Software Switch (BESS)
C++ PIFO implementations is used for scheduling
10Gbps and 40Gbps CloudLab evaluation

## Slide 24: Loom Evaluation
Can Loom drive line rate? Can Loom enforce network policies?
Experiment: Microbenchmarks with iPerf
Can Loom isolate real applications?
Experiment: CloudLab experiments with memcached and Spark
How effective is Loom’s efficient OS/NIC interface?
Experiment: Analysis of PCIe writes in Linux(QPF) versus Loom

## Slide 25: Loom 40Gbps Evaluation
i
Setup:
Every 2s a new tenant starts or stops
Each tenant i starts 4 flows (4-256 total flows)
T2
T1
T3 T4
Fair
Policy: All tenants should receive an equal share.
5
15
20
0
0
40
30
20
10
Throughput
(Gbps)
T4
0
5
15
20
40
30
20
10
0
Throughput
(Gbps)
T1
T4
0
5
15
20
10
Time (seconds)
40
30
20
10
0
Throughput
(Gbps)
SQ
105
105
T1 T2 T3
T4
10
Time (seconds) T1 T2 T3
MQ
10
Time (seconds) T2 T3
Loom

## Slide 26: Application Performance: Latency
109
vs
Latency Sensitive
Bandwidth Hungry
Setup: Linux software packet scheduling (Qdisc) is configured to prioritize memcached traffic over Spark traffic
Pri
0
1000
2000
3000
4000
Loom
Linux (MQ)
90th Percentile Latency (us)

## Slide 27: Loom Interface Evaluation
111
Line-rate | Existing approaches: PCIe Writes per second | Loom: PCIe Writes per second
10 Gbps | 833K | 19K
40 Gbps | 3.3M | 76K
100 Gbps | 8.3M | 191K
Worse case scenario:
Packets are sent in 64KB batches and each packet is from a different flow

## Slide 28: Conclusion
Current NICs cannot ensure that competing applications are isolated
Loom is a new NIC design that completely offloads all packet scheduling to the NIC with low CPU overhead
Loom’s benefits translate into reductions in latency, increases in throughput, and improvements in fairness

## Slide 29: Weakness
DAG policy cannot be enforced network-wide.
Not proof that all algorithms can be expressed by DAG.
Rate-limit design has much to improve:
  Extra enqueue and dequeue operations
  Issues exists in global shaping queue

## Slide 30: Thank you!